R10 	RAINWATER DRAINAGE SYSTEMS

130 	Pressure Assisted Rainwater Drainage System

-	Manufacturer and reference: CGL Systems Ltd, 2 Young Place, Kelvin Industrial Estate, East Kilbride, G75 0TD.

Tel: 01355 235 561, Fax: 01355 247 189

E-mail: web@cglsystems.co.uk

-	The CGL “RainPulse” Pressure Assisted Rainwater Management System consists of a membrane lined gutter, outlets (site fitted) and either HDPE or Aluminium down pipes.  The components form part of the overall system.  The ability of the system to discharge rainwater from the roof to ground drainage is calculated through CGL Systems software on a project-to-project basis.  (Please Consult with CGL Systems Ltd for full project design review)

-    	CGL Systems Ltd Composite Gutter - A prefabricated light-weight self-supporting metal composite insulated construction with a fully bonded, continuous membrane lining to the water-carrying surface.  The gutters are suitable for regular walkway traffic and have minimal maintenance requirements.

-	CGL RainPulse Outlets - Outlets are Pressure Assisted outlets to ensure extracting the water from the gutter and into the pipe is done in the most efficient way.  The system operates at full bore under pressure during storm conditions as detailed in R10 365.

-    	CGL RainPulse Pipe work choices -   HDPE down pipes for internal use or Aluminium Downpipes for external use which can be painted to colour to suit.  Both options detailed in sections R10 415 and 370.

250 	Design Parameters – Pressure Assisted Rainwater Drainage System

-	Design, Fabrication and Supply of a Pressure Assisted rainwater management system for discharging rainwater from the roof to ground drainage.

-	Manufacturer and reference: CGL Systems Ltd, 2 Young Place, Kelvin Industrial Estate, East Kilbride, G75 0TD.

Tel: 01355 235 561, Fax: 01355 247 189

E-mail: web@cglsystems.co.uk

-	System Components:

CGL Systems Ltd Membrane Lined Composite Gutter (R10 325 or H31 234).

CGL RainPulse Outlet (R10 365)

CGL RainPulse HDPE down pipes or CGL RainPulse Aluminium Downpipes (R10 415 or 370).

-	The system must be designed within the following parameters to discharge to underground drainage economically, be regularly self-cleansing and maintenance free in normal use with an annual inspection and clean if necessary.

-	The roof drainage subcontractor will liaise with CGL RainPulse to determine optimum positions of the RainPulse outlets and pipe work. All design calculations are performed using CGL Systems Ltd specifically designed software.

-	The system shall always protect the buildings from the ingress of rainwater both internal and external.

-	Pipe work must remain airtight at maximum and minimum operating pressures. Pipe work must accommodate structural and thermal movement using flexible joints or other suitable means without damage to fixings and joints or excess stress, abrasion, or noise.

-	Design rate of rainfall: As BS EN 12056-3:2000

Geographical Location: (specific to project please complete)

Storm Duration: 2 minutes.

Building life: (specific to project please complete)

Category of risk (specific to project please complete) to BS EN 12056-3:2000

Maximum operational pressure: -0.80 bar gauge m vacuum.

-	Roof outlets: number, location and size to be determined by CGL Systems Ltd Rainwater outlets to be supplied to the roofing contractor for installation prior to pipe work.

## 325 	Composite Gutter

-   	Manufacturer and reference: CGL Systems Ltd, 2 Young Place, Kelvin Industrial Estate, East Kilbride, G75 0TD.

Tel: 01355 235 561, Fax: 01355 247 189

E-mail: web@cglsystems.co.uk

-    	CGL Systems Ltd Composite Gutter - A prefabricated light-weight self-supporting metal composite insulated construction with a fully bonded, continuous membrane lining to the water-carrying surface.  The gutters are suitable for regular walkway traffic and have minimal maintenance requirements. CGL can provide design and specifications for a full RainPulse Rainwater Management service, and it is recommended that they are consulted early in the design process.

-   	Profile: Valley / Box / Boundary wall (Select)

- Type: CGL Systems Ltd Membrane Lined Gutter as part of the CGL RainPulse Rainwater Management System.

- Construction:

External Finish - 1.2mm thick PVC weatherproofing membrane, colour: Light grey.  Factory laminated to 0.6mm/0.9mm or 1.2mm thick galvanised steel to BS EN 10142 grade Fe P02G with Z275 coating.

Insulation – 90mm Polyisocyanurate (PIR) which is CFC and HCFC free providing a “U” value of 0.25 W/m²K. (For alternative “U” values consult with CGL Systems Ltd).

Internal Liner Sheet –

0.7mm thick Polyester coated White Enamel, 20 micron top coat to underside of lining.

-   	Nominal Size(s):  ……mm Girth.  (Consult with CGL Systems Ltd and Insert Sizes).

-   	Accessories:

CGL RainPulse Rainwater Outlets: fitted on site at appropriate locations within the CGL Systems Ltd Gutter.

CGL RainPulse Downpipe System: fitted to CGL Rainwater Outlets on site.  Downpipes either HDPE or Aluminum mill finish or with PPC finish.

Tell tale overflows fitted either in the gutter base or the stop ends.

Support where required: Loose pre-galvanized steel support straps 50 x 6mm flat bar to BS 4360, galvanized to BS 729

-   	Site fixing materials: 4.9mm diameter plated steel rivets, Outlets and overflows which are generally supplied loose for site installation and positioning.

-   	Factory fabricated: Fitted stop ends / mitered corner sections / tee sections / change of section / sumps.

-   	Method of jointing: Form site joints and fit outlets and overflows by riveting the overlap of metal and hot air weld overlapping PVC membrane, leaving a central unbonded strip which allows for expansion and contraction.

-   	Method of fixing: Gutter wings to be pre-fixed to purlin / support steelwork at approximately 300mm centre’s both sides prior to installation of roof liner sheet.

365 	Proprietary Rainwater Outlets

-	Manufacturer and reference: CGL Systems Ltd, 2 Young Place, Kelvin Industrial Estate, East Kilbride, G75 0TD.

Tel: 01355 235 561, Fax: 01355 247 189

E-mail: web@cglsystems.co.uk

-	CGL RainPulse Outlets - Outlets are Pressure Assisted outlets to ensure extracting the water from the gutter and into the pipe is done in the most efficient way.  The system operates at full bore under pressure during storm conditions.  The CGL RainPulse Rainwater Management System incorporates an appropriate gutter, outlets, and pipes to ensure maximum efficiency in the use of all components.  Must be used in conjunction with the CGL RainPulse Gutter as detailed in R10 325 or H31 234 (available from CGL RainPulse) and the CGL RainPulse HDPE or Aluminium downpipe system (see R10 415 or 370) with associated pipe clip sets.

-	Outlet Components:

Spigots are manufactured in Aluminium grade BS1050 in 2/3mm.

Anti-vortex plate and clamp rings are manufactured from die cast aluminium LM6 BS1490-1998.

-	Roof construction: RainPulse outlets fitted into CGL Membrane Lined Gutter system as detailed in R10 320.

-	Size: Determined by CGL RainPulse as part of the specific building design calculation performed by CGL Systems Ltd and denoted on working drawings. (Consult with CGL Systems Ltd).

Please select from the following 2 options for pipe work

370 	Aluminium Pipework

-	CGL RainPulse Rainwater Management System incorporating the CGL Systems Ltd Gutter as detailed in R10 325 or H31 234 (available from CGL Systems), the CGL RainPulse Outlet and the CGL RainPulse Aluminium downpipe system with associated pipe clip sets.

-	Type and Thickness: Pipes are Aluminium Tubes 6063-T6 with a wall thickness of 1.6mm.  Fittings are manufactured from 2mm Aluminium, minimum grade 1050

-	Manufacturer and reference: CGL Systems Ltd, 2 Young Place, Kelvin Industrial Estate, East Kilbride, G75 0TD.

Tel: 01355 235 561, Fax: 01355 247 189

E-mail: web@cglsystems.co.uk

-	Nominal Size:  Outside pipe diameters options are 76.2, 88.9 and 101.6mm Aluminium tube as determined by CGL RainPulse as part of the building design and denoted on working drawings. (Consult with CGL Systems Ltd).

-	Accessories:

Flex-seal couplings or equal approved joint for connection to underground.

Bond It Multi-Mate high modulus general purpose silicone sealant as supplied by CGL Systems Ltd.

-	Finish: The aluminium pipes can either be supplied in a mill finish or be Polyester Powder Coated to a RAL colour.  (PPC colour to be added here)

-	Method of jointing: Apply above stated silicone sealant to pipe end and insert into Push fit sleeves to appropriate depth ensuring air tightness.

-	Brackets: Proprietary M10 bracket pipe clip sets available from CGL Systems Ltd.

415 	HDPE Pipework

-	CGL Systems Ltd Rainwater Management System incorporating the CGL Systems Ltd Gutter as detailed in R10 325 or H31 234 (available from CGL Systems), the CGL RainPulse Outlet and the CGL RainPulse HDPE downpipe system with associated pipe clip sets.

-	Pipe and fittings: HDPE to DIN 4102-B2, DIN19537, S12.5 BD EN1519, PE80 Wall thickness and diameter and marked accordingly along the length of the pipe.  BBA certificate number 92\2796

-	Manufacturer and reference: CGL Systems Ltd, Merson Group, 2 Young Place, Kelvin Industrial Estate, East Kilbride, G75 0TD.

Tel: 01355 235 561, Fax: 01355 247 189

E-mail: web@cglsystems.co.uk

-	Nominal Size:  Outside pipe diameter options are 75, 90 and 110mm HDPE as determined by CGL Systems as part of the building design and denoted on working drawings. (Consult with CGL Systems).

-	Brackets: Proprietary M10 bracket pipe clip sets available from CGL Systems.

-	Accessories:

Flex-seal couplings or equal approved joint for connection to underground.

Push fit jointed fittings, as appropriate.

Bond It Multi-Mate high modulus general purpose silicone sealant as supplied by CGL RainPulse.

-	Method of jointing: Apply above stated silicone sealant to pipe end and push fit into sleeves with EPDM ring seal to appropriate depth ensuring air tightness.